## Slide 1
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
The 8051 Microcontroller
Chapter 2 Hardware Summary
Ref. I. Scott Mackenzie, The 8051 Microcontroller

## Slide 2
Features of 8051
2
Ref. I. Scott Mackenzie
4KB ROM
128 bytes RAM
Four 8-bit I/O ports
Two 16-bit timers
Serial interface
64KB external code memory space
64KB external LdêaChtaí Thmôngemory space

## Slide 3
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Comparison of MCS-51 Family
3
Ref. I. Scott Mackenzie

## Slide 4
FIGURE 2–1 8051 block diagram
PSEN’ - use external Program memory ALE – Address/Data multiplexing
EA’ – 5V for internal ROM, 0V for external ROM
4
Ref. I. Scott Mackenzie

## Slide 5
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
51 pinouts
Address/Data Buses Multiplexing
Parallel I/O
Serial I/O
5
FIGURE 2–2 80
Ref. I. Scott Mackenzie

## Slide 6
Around The Pins
Port 0: dual purpose
  I/O port
  Multiplexed address and data bus (AD0-AD7)
Port 1: I/O port
Port 2: dual purpose
  I/O port
  High-byte address bus (A8-A15)
6
Ref. I. Scott Mackenzie

## Slide 7
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Port 3: dual purpose
7
Ref. I. Scott Mackenzie

## Slide 8
/PSEN (Program Store Enable)
o Connects to /OE (Output Enable) of EPROM to permit reading of program bytes
8
Ref. I. Scott Mackenzie

## Slide 9
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
ALE (Address Latch Enable)
o Use to demultiplex the address and data bus
9
Ref. I. Scott Mackenzie

## Slide 10
/EA (External Access) It is tied to +5V or ground.
  /EA = +5V: executes programs from internal ROM
  /EA = 0V: executes programs from external ROM
10
Ref. I. Scott Mackenzie

## Slide 11
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
RST (Reset):
11
Ref. I. Scott Mackenzie

## Slide 12
XTAL1 , XTAL2: On-chip oscillator inputs
12
Ref. I. Scott Mackenzie

## Slide 13
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
FIGURE 2–5 Relationship between oscillator clock cycles, states, and the machine cycle
A machine cycle is 12 oscillator periods. Use 12 MHz crystal: a machine cycle is 1 µs
13
Ref. I. Scott Mackenzie

## Slide 14
Vdd, Vss: Power connections
  Vdd is connected to +5V
  Vss is connected to ground (0V)
14
Ref. I. Scott Mackenzie

## Slide 15
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
I/O Port Structure
Port 1, 2, and 3 have internal pull-up resistors.
Port 0 has no internal pull-up resistors.
Instructions that input a port bit require the ‘1’ port latch.
15
Ref. I. Scott Mackenzie
Don’t need Bus-driver

## Slide 16
Memory Organization
Memory
  ROM: for program (code) € Code memory
    External: maximum 64K
    Internal (on-chip): depend on chips
  RAM: for data € Data memory
    External: maximum 64K
    Internal (on-chip): depend on chips
16
Ref. I. Scott Mackenzie

## Slide 17
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
FIGURE 2–6 Summary of the 8031 memory spaces
Memory Map
256-byte
64-Kbyte
17
Ref. I. Scott Mackenzie

## Slide 18
Internal (on-chip) data memory
  Register banks (00H-1FH)
  Bit-addressable RAM (20H-2FH)
  General-purpose RAM (30H-7FH)
  Special function registers (80H-FFH)
18
Ref. I. Scott Mackenzie

## Slide 19
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Bit-addressable RAM
(20H-2FH)
Register banks (00H-1FH)
DPTR
Using for MUL,DIV
Internal (on-chip) data memory:
General purpose RAM
(30H-7FH)
Special function registers (80H-FFH)
19
Ref. I. Scott Mackenzie

## Slide 20
General purpose RAM
  80 bytes from addresses 30H to 7FH
  Accessed using direct or indirect addressing modes Ex:
Direct
MOV A, 5FH
Indirect
MOV R0, #5FH MOV A, @R0
20
Ref. I. Scott Mackenzie

## Slide 21
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Bit-addressable RAM
  16 bytes from (byte) addresses 20H to 2FH
  128 bits from bit addresses 00H to 7FH
  Bit can be set, cleared, ANDed, ORed, … Ex:
To set bit 67H
SETB 67H
or
MOV A, 2CH
ORL A, #10000000B MOV 2CH, A
21
Ref. I. Scott Mackenzie

## Slide 22
22
Register banks
  Bank 0 (default), Bank 1, Bank 2, and Bank 3
  Change register bank by selecting bits RS1 and RS0 the program status word
  One bank includes 8 registers: R0 through R7 Ex:
Read the contents of location 05H into the accumulator
MOV A, R5
or
MOV A, 05H
Write the contents of the accumulator into location 00H
MOV R0, A
Ref. I. Scott Mackenzie

## Slide 23
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Special Function Registers
Program Status Word (PSW)
A and B registers
Stack Pointer (SP)
Data Pointer DPTR = DPH:DPL
Port Registers (P0, P1, P2, P3)
Timer Registers (TMOD, TCON, Timer1=TH1:TL1, Timer0 = TH0:TL0)
Serial Port Registers (SCON, SBUF)
Interrupt Register (IE, IP)
Power Control Register (PCON)
23
Ref. I. Scott Mackenzie

## Slide 24
Program Status Word (PSW)
24
Ref. I. Scott Mackenzie

## Slide 25
ĐH Bách Khoa - ĐHQG TP.HCM
A and B Register
  A (accumulator) register (Address E0H)
    The most versatile register
    Used for many operations (addition, subtraction, multiplication, division, Boolean bit manipulations, …)
  B register (Address F0H)
    Used with the A register for multiplication and division
Ex: To multiply the 8-bit unsigned values in A and B and leaves the 16-bit result in A (low-byte) and B (high-byte)
MUL AB
To divide A by B and leaves the integer result in A and the remainder in B
DIV AB
25
Ref. I. Scott Mackenzie

## Slide 26
26
Stack Pointer (SP) (Address 81H)
  Used to access the stack
  PUSH: SP increases before storing data on the stack
  POP: data is read from the stack and then SP decreases
  The reset value of SP is 07H € Stack is from 08H
  LIFO: Last In First Out
Ex: To set the stack beginning at 60H
MOV SP,#5FH
To store data from R1 register into stack
PUSH 01H
To retrieve data from stack to register R2
POP 02H
Ref. I. Scott Mackenzie

## Slide 27
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Stack Pointer (SP) (Address 81H)
R1,#67H R3,#0D8H R7,#63H
Ex: MOV R1,#15H MOV R3,#0FH MOV R7,#0E9H PUSH 01H
PUSH 03H PUSH 07H
… MOV MOV MOV
…
POP 07H
POP 03H
POP 01H
27
R1
15H
R3
0FH
R7
E9H
0AH
09H
08H SP=07H
15H
0AH
09H SP=08H
07H
0FH
15H
0AH
SP=09H
08H
07H
R1
67H
R3
D8H
R7
63H
E9H
0FH
15H
SP=0AH
09H
08H
07H
R1 15H
R3
0FH
R7
E9H
Ref. I. Scott Mackenzie

## Slide 28
Stack Pointer (SP) (Address 81H)
Ex: MOV R1,#15H MOV R3,#0FH PUSH 01H PUSH 03H
POP 01H
POP 03H
28
R1
15H
R3
0FH
0AH
09H
08H SP=07H
15H
0AH
09H SP=08H
07H
0FH
15H
0AH SP=09H
08H
07H
R1
0FH
R3
15H
Ref. I. Scott Mackenzie

## Slide 29
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Data Pointer (DPTR) (Addresses 82H & 83H)
  Used to access external code or data memory
  DPTR is 16-bit register, including DPH (high-byte) and DPL
(low-byte)
Ex: To write 55H into external RAM location 1000H
MOV A,#55H MOV DPTR,#1000H
MOVX @DPTR,A
29
Ref. I. Scott Mackenzie

## Slide 30
Port Register
  P0, P1, P2, and P3 registers
  Used to access I/O ports
  Ports 0, 2, and 3 may not available for I/O if external memory is used or if some of special features are used (interrupt, …)
  All ports are bit-addressable
Ex: To read data from Port 1 into A register
MOV A,P1
To write data from R7 register to Port 2
MOV P2,R7
To set bit 7 of Port 3
SETB P3.7
To clear bit 7 of Port 1
CLR P1.7
Ref. I. Scott Mackenzie
or CLR 97H
30

## Slide 31
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Timer Registers
  8051 contains two 16-bit timer/counters: Timer 0 & Timer 1.
  Used for timing intervals or counting events
  Timer 0 = TH0 (high-byte) & TL0 (low-byte)
  Timer 1 = TH1 (high-byte) & TL1 (low-byte)
  Timer operation is set by the Timer Mode Register (TMOD) and the Timer Control Register (TCON) (discussed in details in Chapter 4).
31
Ref. I. Scott Mackenzie

## Slide 32
Serial Port Registers
  8051 contains serial port for communicating with serial devices such as PC (via serial port) or other ICs with serial interface.
  The Serial Control Register (SCON) is used to set various modes of operations.
  The Serial Buffer Register (SBUF) is used to transmit and receive data.
    Writing to SBUF loads data for transmission
    Reading SBUF accesses received data (discussed in details in Chapter 5)
32
Ref. I. Scott Mackenzie

## Slide 33
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Interrupt Registers
  8051 has a 5-source, 2-priority level interrupt structure.
  The Interrupt Register (IE) is used to enable interrupts.
  The Interrupt Priority Register (IP) is used to set the priority level.
(discussed in details in Chapter 6)
33
Ref. I. Scott Mackenzie

## Slide 34
Power Control Register (PCON)
34
Ref. I. Scott Mackenzie

## Slide 35
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
External Memory
When external memory is used:
  Port 0 is a multiplexed address (A0-A7) & data (D0-D7) bus.
  Port 2 is usually the high-byte of address bus (A8-A15)
35
Ref. I. Scott Mackenzie

## Slide 36
Accessing External Code Memory
  External code memory is ROM enabled by /PSEN signal.
  Port 0 & Port 2 are unavailable as I/O ports.
  Port 0 is AD0-AD7 bus & Port 2 is A8-A15 bus.
36
Ref. I. Scott Mackenzie

## Slide 37
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
FIGURE 2–10 Read timing for external code memory
Timing diagram for external CODE memory access
37
Ref. I. Scott Mackenzie

## Slide 38
Accessing External Data Memory
  External code memory is RAM enabled by /RD & /WR
signals using MOVX instruction.
  Port 0 & Port 2 are unavailable as I/O ports.
  Port 0 is AD0-AD7 bus & Port 2 is A8-A15 bus.
38
Ref. I. Scott Mackenzie

## Slide 39
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
FIGURE 2–11 Timing for MOVX instruction
For external DATA memory
39
Ref. I. Scott Mackenzie

## Slide 40
Address Decoding
  If multiple ROMs and/or RAMs are interfaced to an 8051,
address decoding is required.
  Typically, a decoder IC such as 74HC138 is used with its outputs connected to the chop select (/CS) inputs on the memory ICs.
  Remember enable lines: /PSEN for code memory (ROM) and
/RD & /WR for data memory (RAM)
  Accommodate up to 64KB each of ROM and RAM
40
Ref. I. Scott Mackenzie

## Slide 41
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
FIGURE 2–13 Address decoding
ROM
RAM
41
Ref. I. Scott Mackenzie

## Slide 42
Overlapping the External Code and Data Spaces
o A RAM can occupy code and data memory space by using the following circuit.
For external CODE and DATA memory
42
Ref. I. Scott Mackenzie

## Slide 43
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
43
FFH 80H | Special Function Registers (SFRs)
7FH 30H | General Purpose RAM
2FH 20H | Bit Addressable RAM
1FH 00H | Register banks
Address
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
32H
One memory location
8-bit content
Internal RAM
256 locations from address 00H to FFH
The content of one location is 8 bit.
Address

## Slide 44
Register banks (00H-1FH)
General purpose RAM (30H-7FH)
Bit- addressable RAM
(20H-2FH)
Special function registers (SFRs) (80H-FFH)
44

## Slide 45
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
General Purpose RAM
Address from 30H to 7FH
The content of one location is 8 bit.
Ex: MOV A,30H
This instruction moves (reads) the content of location 30H (NOT data 30H) to register A.
A 30H
Ex: MOV 31H,R4
This instruction moves (writes) the content of register R4 to location 31H.
31H
R4
45

## Slide 46
Register banks (00H-1FH)
General purpose RAM (30H-7FH)
Bit- addressable RAM
(20H-2FH)
Special function registers (SFRs) (80H-FFH)
46

## Slide 47
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Ex: SETB 20H.0
or SETB 00H
Ex: MOV C,31H
or MOV C, 26H.1
Bit Addressable RAM
Address from 20H to 2FH
The content of one location is 8 bit.
Can read/write a byte or a bit
Ex: MOV 20H, A ; writes the content of register A to location 20H.
20H A
 |  |  |  |  |  |  | 1
20H
Not affected
26H
CY
47

## Slide 48
Register banks (00H-1FH)
General purpose RAM (30H-7FH)
Bit- addressable RAM
(20H-2FH)
Special function registers (SFRs) (80H-FFH)
48

## Slide 49
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
R0 of Bank 0 is location 00H
…
R7 of Bank 0 is location 07H
R0 of Bank 1 is location 08H
…
R7 of Bank 1 is location 0FH
R0 of Bank 2 is location 10H
…
R7 of Bank 2 is location 17H
R0 of Bank 3 is location 18H
…
R7 of Bank 3 is location 1FH
Register Banks
4 banks: Bank 0 (default), Bank 1, Bank 2, and Bank 3
Change register bank by selecting bits RS1 and RS0 (in register PSW)
One bank includes 8 registers: R0 through R7
49

## Slide 50
Register Banks – Your Turn!
R1 of Bank 0 is location ………
R5 of Bank 0 is location ………
R5 of Bank 1 is location ………
R1 of Bank 2 is location ………
R2 of Bank 3 is location ………
R6 of Bank 3 is location ………
50

## Slide 51
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
=
Register Banks
Ex: use default bank (Bank 0)
R5
05H
≡
MOV A, R5 =
Read the contents of register R5 into the accumulator
MOV A, 05H
Read the contents of location 05H into the accumulator
MOV R0, A
Read the contents of register A into register R0
MOV 00H, A
Read the contents of register A into location 00H
51

## Slide 52
Register PSW (Program Status Word)
52

## Slide 53
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Ex: MOV
PSW, #00010000B ; select bank 2
or SETB RS1
CLR RS0
Try it: Select bank 1
……………………..
……………………..
Selecting Register Bank
The active bank is selected by bit RS1 (PSW.4) & RS0 (PSW.3)
RS1 | RS0 | Bank
0 | 0 | 0
0 | 1 | 1
1 | 0 | 2
1 | 1 | 3
53

## Slide 54
Register banks (00H-1FH)
General purpose RAM (30H-7FH)
Bit- addressable RAM
(20H-2FH)
Special function registers (SFRs) (80H-FFH)
54

## Slide 55
ĐH Bách Khoa - ĐHQG TP.HCM
- chithong@hcmut.edu.vn
Special Function Registers (SFRs)
SFRs include register A, B, PSW, P0, P1, P2, P3, DPTR, TMOD, SCON …
All SFRs are accessible by name and direct address.
Both of them must be coded as direct address
Ex: MOV P1, A ; Output register A to Port 1 MOV 90H, A ; same
€ Same opcode: F5 90 Ex: MOV R1, ACC
MOV R1, 0E0H
€ Same opcode: A9 E0 Ex: MOV R1, ACC
MOV R1, A
€ Same function BUT different opcodes (A9 E0 vs. F9)
Try it: Input Port 2 to register A ……………………………
55

## Slide 56
56
References
I. Scott Mackenzie, The 8051 Microcontroller
Các tài liệu trên Internet không trích dẫn hoặc không ghi tác giả